## Slide 1
STERILIZATION
&
DISINFECTION

## Slide 2
Any procedure that reduces pathogenic microbes to a level where items are safe for handling & disposal.
It can be achieved by cleaning, disinfection and sterilization.
A process that removes foreign material (dirt, organic matter).
Must precede disinfection and sterilization.
Usually done with soap and water or detergent.
Decontamination
Cleaning

## Slide 3
Destruction of most but not necessarily all pathogenic microbes or their spores.
Killing of all living forms of microbes including spores.
Disinfection
Sterilization

## Slide 4
Chemical compounds that could be applied topically on animate surfaces.
Chemical compounds applied for inanimate surfaces.
Antiseptics
Disinfectants

## Slide 5
Importance of sterilization and disinfection:
Safety in the laboratory.
The patient safety depends on using proper methods of sterilization to prepare instruments, needles, IV fluids.
The accuracy and validity of microbiological tests.

## Slide 6
DISINFECTION
Heat
Moist heat at temperature below 100 degree (Pasteurization).
Moist heat at temperature of 100 degree
  Boiling
  Steaming
Radiation: (Ultraviolet rays)
Chemical: (Disinfectants)

## Slide 7
Moist heat at temperature below 100 degree
Used for milk disinfection.
Milk is heated either at 63 degree for 30 minutes or 72 degree for 20 seconds and immediately cooled to below 10 degree.
Disinfection by heat
Pasteurization

## Slide 8
Moist heat at temperature 100 degree:
Heating at 100 degree for 20 minutes.
Used for disinfection of surgical and medical equipments in emergency.
Boiling

## Slide 9
Done in Koch’s sterilizer.
This sterilizer is vertical metal cylinder with removable conical lid having a small opening for escaping steam.
The articles to be sterilized are placed on a perforated tray situated above water which is placed in the bottom of the cylinder.
Steaming

## Slide 10
(Tyndallization)
Intermittent sterilization by exposure to steam at 100 degree for 20-45 min. for three successive days.
Used for sterilization of sugar media which decompose at high temperatures.
The principle is that one exposure will kill only vegetative bacteria. Between heatings, the spores will vegetate to be killed during subsequent exposure.

## Slide 11
Present in sun rays or artificially produced by
mercury lamp have weak penetrating power.
Used to reduce the number of bacteria in air inside operation rooms, laboratory safety cabinet.
Disinfection by radiation
Ultraviolet rays

## Slide 12
Disinfectants may be:
High level disinfectants.
Intermediate level disinfectants.
Low level disinfectants.
Disinfection by chemical disinfectants

## Slide 14
Prions (the most resistant)
Spores
Tubercle bacilli
Non enveloped viruses
Fungi
vegetative bacteria
Enveloped viruses such as HBV, HIV
Organisms according to the innate resistance
Most resistant
Least resistant

## Slide 15
Ethyl alcohol or isopropyl alcohol 70%.
Used as skin antiseptic.
Intermediate level disinfectant.
Exposure for at least 5 minutes is needed to achieve adequate disinfection.
Alcohol
1

## Slide 16
Available in 2% concentration (cidex).
High to intermediate level disinfectant.
Disinfection of instruments that can not withstand heat such as endoscopes.
Glutaraldehyde
2

## Slide 17
Example of chlorine releasing compounds is:
  Hypochlorite solution (such as household bleach)
Intermediate level disinfectant.
Widely used in homes, hospitals and laboratories to disinfect table tops, incubators, spilled cultures.
Disinfection of water supply.
Chlorine releasing compounds
3

## Slide 18
Examples of iodophores:
  Tincture iodine (2% iodine in ethanol)
  Betadine (10% povidone-iodine)
Intermediate to low level disinfectant.
Used for disinfection of surgical wounds.
Iodophores
4

## Slide 19
Example:
  Dettol, lysol (2% concentration)
Intermediate level disinfectant.
Used in laboratories to disinfect spilled cultures on working areas or in discard jars.
Phenolic compounds
5

## Slide 20
Example:
  Cetavlon, savlon
Low level disinfectant.
Used to clean floors, walls.
Inactivated by organic matter.
Not affect Gram negative bacilli.
Quaternary ammonium compounds
6

## Slide 21
Available as 3% H2O2
High to intermediate level disinfectant.
Used as antiseptic for wounds, disinfecant for contact lenses.
Hydrogen peroxide
7

## Slide 22
As mecury in mercurochrome and silver in silver nitrate.
Safe antiseptic used for hygienic and surgical hand washing and for oral hygiene.
Heavy metals
8
Chlorhexidine
9

## Slide 23
STERILIZATION
Chemical methods (Cold sterilization)
Heat
Dry heat (Red heat, hot air oven, incineration)
Moist heat at temperature above 100 degree (Autoclave)
Radiation: (Ionizing radiation & infrared rays)
Filtration : (Fluid filters & air filters)
Gaseous sterilization : (Ethylene oxide + gas plasma)

## Slide 24
Glutaraldehyde (contact time 10 hours).
Liquid peracetic acid.
H2O2 6%.
Chemical sterilization

## Slide 25
Sterilization by heat
Dry heat
Moist heat

## Slide 26
Less effective than the moist heat.
Examples of dry heat are:
Red heat:
  Sterilization of the bacteriological loop by heating in the Bunsen flame or electric incinerator till becomes hot red.
Dry heat

## Slide 27
Hot air oven:
  Temperature of 160 degree for 2 h. or 170 degree for 1 h.
  For glass ware, and metallic instruments.
Incineration:
    Destruction of contaminated materials in the incinerator.

## Slide 28
Principle:
  When water is heated in a closed vessel under pressure, the boiling point of water rises above 100 degree.
  Water is heated at 2 atmospheric pressure and the boiling temperature will be 121 degree or at 3 atmospheric pressure and the boiling temperature will be 134 degree.
Moist heat (Autoclave)

## Slide 29
Autoclaving is highly efficient because:
  High temperature.
  High penetrating power of the steam under pressure.
  When steam condenses on the articles, it liberates latent heat to the articles to be sterilized.
  Non toxic
  Not time consuming.

## Slide 30
Simple laboratory autoclave

## Slide 31
Directions for use of the simple laboratory autoclave:
  It is a metal cylinder with tightly fitting lid. The lid is connected to a steam discharge tap, safety valve and manometer.
  Water is placed in the bottom and the articles to be sterilized are placed on top of a perforated tray above water level, then the lid is tightly closed.
  Water is heated electrically.

## Slide 32
  The steam discharge tap is opened and the safety valve is adjusted to 15 ib per square inch= double atmospheric pressure.
  Steam will come out of the tap in interrupted jets as it mixes with air.
  When steam is released in a continuous stream, the tap is closed.
  When the steam pressure reaches the desired level, safety valve will allow excess steam to escape.

## Slide 33
  From this point, the holding sterilization time which is 20-30 minutes is calculated.
  Then, the heater is turned off and the autoclave is allowed to cool down before opening the lid.
  Autoclave is used for sterilization of:
  Surgical instruments and dressings.
  Bed linen.
  Cotton, gauze
  Culture media not destroyed by heat.

## Slide 34
Steam jacketed autoclave:
  Double walled chamber in which steam at 121 degree is introduced from an external source.
  Steam enters the jacket from which it enters the chamber migrating downwards replacing the air which is expelled through a discharge tap at the bottom.
Flash autoclaves:
  It sterilizes at 134 degree for 3 – 5 minutes.
  Used in operation rooms in emergency situations.

## Slide 35
Testing the efficiency of autoclave:
Mechanical methods:
  Daily measurement of temperature, pressure gauge.
Chemical indicators:
  Change its color at the end of sterilization cycle.
Biological indicators:
  Using spores of Bacillus stearothermophilus.
  However, spores of Bacillus subtilis are used to test the efficiency of hot air oven.

## Slide 36
Ionizing radiation:
Such as gamma rays emitted from radioactive cobalt 60 or beta rays emitted from electron accelerators.
High penetrating power.
Used for plastic syringes, catheters, gloves, surgical sutures.
Sterilization by radiation

## Slide 37
Used for sterilization of biological fluids destroyed by heat such as serum, plasma, vitamins, hormones.
Air is filtered by HEPA filters.
HEPA means high efficiency particulate air way arresters.
Air filtration is needed in operation rooms, safety cabinets.
Sterilization by filtration
Fluid filters
Air filters

## Slide 38
Vacuum or Seitz filter:
  Formed of asbestos disc which is inserted into a metal holder connected to a flask.
Fluid filters

## Slide 39
Millipore (membrane) filters:
  Synthetic membranes made from cellulose diacetate.
Syringe filter:
  Membrane filters 13 – 25 mm in diameter in a small holder connected to a syringe containing the fluid to be filtered.

## Slide 40
Used for plastic and rubber articles.
Ethylene oxide gas is toxic, explosive and carcinogenic to laboratory animals.
Plasma means any gas which is formed of ions, electrons, neutral particles.
Used for surgical instruments mainly those with narrow lumen such as arthroscopes & laparoscopes.
Non toxic.
Sterilization by gases
Ethylene oxide gas
Plasma gas sterilizer

## Slide 41
Selection of adequate level of contamination
Item | Characteristics | Example | methods
Critical | Instruments that enter sterile tissues, cavities or vascular system | Surgical instruments, needles, catheters | Sterilization by autoclave, plasma gas sterilizer or ethylene oxide gas
Semi critical | Objects that come in contact with non intact skin or mucous membranes | Endoscopes, thermometers | High level disinfection
Non critical | Objects that come in contact with intact skin | Sphygmomanometer, bed linen | Intermediate to low level disinfection