## Slide 1: Field-Programmable Gate Arrays (FPGAs)
Fine-grained reconfigurable hardware
Gate-Array: regular structure of “logic cells”, connected through an interconnection network
Configuration stored in SRAM, must be loaded on startup
Notes: <number>

## Slide 2: Field Programmable Gate Arrays
Evolved from PALs, PLDs, Complex PLDs
A niche hardware implementation technology
  Strengths: quick prototyping and time-to-market,
reprogrammability, relatively easy to use
  Weaknesses: cost, density, speed
Vendors: Xilinx, Altera, Actel, Atmel, Lucent,
Cypress, Quick Logic, IBM, Motorola

## Slide 3: FPGA Technologies
Programmable Elements
  Logic blocks
    combinatorial: lookup tables (LUTs) or gates + muxes
    sequential: flip-flops
  Interconnect: metal wire segments connected by...
    pass transistors driven by SRAM or EEPROM bit cells
    fuses or antifuses (one-time programmable)
FPGA architecture variations
  CLB arrays, rows, macrocells; fine/coarse grain
  RAM, fast wide adders, TBUFs (3-state buffers)

## Slide 4: FPGA Applications
Conventional: cheap, fast turnaround, field
upgradeable ASICs (J32)
Some reconfigurable applications
  Quickturn: fast design simulation/verification
  Signal, image processing: filters, warping, music
  Graphics: span and octtree rendering acceleration
  Military: target dependent correlation/recognition
  Cryptography: DES search
  “Hardware” genetic algorithms

## Slide 5: A Generic FPGA Architecture
An FPGA architecture consists of
  programmable IO,
  programmable logic, and
  programmable routing.
Each programmable block is also called configurable logic block (CLB)
  contains a group of logic elements,
  each logic element contains one k-input lookup table, which can implement any logic function up to k variables.
The wire segments in the routing channels are connected by programmable switches.
The programmability usually is provided through a large amount of SRAM cells on the chip.

## Slide 7: FPGA Device Configuration
SRAM-based FPGA devices must be configured each time the board powers up:
  When the board is powered on, the configuration device will automatically send a serial data stream to the FPGA device and configure it.
  Store the configuration data in on-board memory and use another PLD (typically an EPROM-based device, or a microprocessor) to act as the controller. When the board is powered on, the controller device will send the configuration data from memory to the targeted FPGA device.
Antifuse-based Technology (e.g., ActelTM, QuicklogicTM):
  an antifuse remains in a high-impedance state until it is programmed into a low-impedance or “fused” state.
  This technology can be used only once on one-time programmable (OTP) devices;
  It is less expensive than the RAM technology.

## Slide 9: Look Up Table (LUT)

## Slide 10: FPGA Advantages
Small development overhead
No NRE (non-recurring engineering) costs
Quick time to market
No minimum quantity order
Reprogrammable

## Slide 11: Xilinx XC2S100-5TQ144 FPGA
2.5 V 144-Pin quad flat pack, 92 I/Os
20R x 30c array of config logic blocks (CLBs)
  Each with 2 slices ,each with 2 logic cells.
  Each cell with a 4-input lookup table (LUT), flip flop.
  Two LUTs = one 16 x 1 dual port RAM.
10 Block RAMs
  Dual ported , 4kb(256x16b),0 cycle latency.
Programmable interconnect
  Hierarchical, plus buses via TBUFs(3-state buffers).